   BIT MANIPULATION IN C

In C programs, “n & m” does the AND operation between binary rep’s of n and m.
- “n | m” does OR operation between binary rep’s of n ,m
- “n ^m” does EXOR operation between binary rep’s of n, m.
- “~n” means the 1’s complement of binary rep’s of n.
- “n << i”, does the left shift of binary rep’s of integer n by ‘i’ bit positions.
  Left shift by ‘i’ positions is done by removing ‘i’ most significant bits of register, followed by shifting all remaining bits to left by ‘i’ positions, & then filling up empty least significant bit in the rightmost positions by zero.
- “n >> i”, does the right shift of binary rep’s of integer n by ‘i’ bit positions.
  Right shift by ‘i’ positions is done by removing ‘i’ most significant bits of register, followed by shifting all remaining bits to right by ‘i’ positions and thereafter filling vacant most significant bit positions by zero.
- In C program, functions like printf, scanf, the format string decides how the data is interpreted.
  “%d” treats data as signed decimal number.
  “%u” treats data as unsigned decimal number
  “%x” treats data as hexadecimal number
  “%o” treats data as octal number
  However there are no format string to print binary numbers as such.
- The integer constants 1) decimal constants should not begin with 0, eg: 25, 12 etc.
  2) octal constants should begin with 0, eg: 012, 073, 077 etc.
  3) Hexadecimal constants should begin with 0x, eg: 0xF, 0xFF, 0x3A
- “printf(“%d”, 011)” prints value 9(decimal, since %d is used as format string) because ‘011’ is interpreted as octal integer constant.
  “printf(“%o”, 9)” prints value 11(octal, since%o is used as format string) because ‘9’ is interpreted as decimal integer constant.

- Binary representation of a number when ANDed with 1 ( n & 1) gives LSB of the binary rep of the number.
- To print out ‘i’th bit of binary rep of a number:- right shift the number by i bit positions , AND with 1
  ie, n = n >> i;
  n = n & 1;
- To set ‘i’th bit of binary of a number to 1 :- left shift 1 by ‘i’ bit positions, OR with obtained bit pattern.
  Ie, p = 1 << i;
  n = n & p;

To set ‘i’th bit of binary of a number to 0 :- left shift 1 by ‘i’ bit positions, 1’S COMPLEMENT the obtained pattern, AND it to binary representation of number
ie p = 1 << i;
p = ~p;
n = n & p;